## Slide 1: Lecture 25: Digital Control 2
ME/AE 6705
Introduction to Mechatronics
Dr. Jonathan Rogers

## Slide 2: Lesson Objectives
Derive the pulse transfer function of PID controller (transfer function of PID in z domain)
Be able to simulate discrete-time systems including feedback control elements
Simulate several discrete feedback systems and examine control performance
  As a function of controller gains
  As a function of sampling time
  Examine tradeoffs
  Discuss effects of control saturation

## Slide 3: Review: Pulse Transfer Functions
Recall from last lecture that pulse transfer function is the z-domain transfer function for a system
C(s)
R(s)
K
Sampler
Proportional Controller
ZOH
(T = 1 sec)
Plant
Transfer Function
Pulse Transfer Function

## Slide 4: Review: Pulse Transfer Function
PTF provides the z-domain poles and zeros for the system
Important: Both s and z domain representations of system are equally valid!
  For systems involving samplers, it is easier to analyze system stability, response, etc in z domain than s domain
…
…

## Slide 5: Pulse Transfer Function of PID
Analog (continuous time) form of PID controller:
Before we can compute the PTF, need to specify how we are going to implement discretization
  This can of course be done in multiple ways
  Does more than one PTF exist for the above PID controller?

## Slide 6: Pulse Transfer Function of PID
Analog (continuous time) form of PID controller:
Before we can compute the PTF, need to specify how we are going to implement discretization
  This can of course be done in multiple ways
  Does more than one PTF exist for the above PID controller?
Yes. Various integral approximations may be used (rectangular, trapazoidal, etc) and various derivative approximations may be used (1st order backward, 2nd order backward, etc.)

## Slide 7: Pulse Transfer Function of PID
Proportional error is sampled:
Select:
First-order finite difference:
Trapazoidal integral approximation:

## Slide 8: Pulse Transfer Function of PID
Taking the z transform:

## Slide 9: Pulse Transfer Function of PID
Computing integral term:
where
and
From table of z Transforms:
where

## Slide 10: Pulse Transfer Function of PID
Thus z transform of integral controller is:
Putting it all together:
Some algebra involved here.
Redefining:

## Slide 11: Digital PID Controllers
This is digital PID controller PTF. We can change gains to affect closed-loop system response.
X(z)
Y(z)
GD(z) Digital PID Controller
G(z) PTF of Plant

## Slide 12: Digital PID Controllers: Example 1
Consider first order system controlled using (digital) integrator only
Simulate system
  Determine integral gain needed for desirable response.
  Explore stability tradeoffs (T vs KI)
X(z)
Y(z)
Digital integrator
First-order plant with ZOH input

## Slide 13: Digital PID Controllers: Example 1
Step 1: Derive PTF of plant.
X(z)
Y(z)
E(z)
U(z)

## Slide 14: Digital PID Controllers: Example 1
Step 2: Write out difference equations for controller and plant.
What is the (continuous-time) alternative to difference equations?

## Slide 15: Digital PID Controllers: Example 1
Simulation code
y = 0 ;
T = 0.5 ;
r = 1 ;
ki = 2 ;
e = r-y ;
t = 0;
u = ki*e ;
tf = 8;
i=2 ;
while(t(end)<tf);
% Calculate state dynamics
y(i) = exp(-T)*y(i-1) + u(i-1) - exp(-T)*u(i-1) ;
% Compute error
e(i) = r-y(i) ;
% Compute control
u(i) = ki*e(i) + u(i-1) ;
t(i) = t(i-1)+T ;
i = i + 1;
end
Simulating discrete-time systems is a lot easier than continuous-time systems.

## Slide 16: Digital PID Controllers: Example 1
T = 1 sec
KI = 0.5
T = 1 sec
KI = 1.5
T = 1 sec
KI = 3.0
T = 1 sec
KI = 6.0
Gains clearly have effect on system stability.

## Slide 17: Digital PID Controllers: Example 1
T = 0.4 sec
KI = 5.0
T = 0.6 sec
KI = 5.0
T = 0.8 sec
KI = 5.0
T = 1 sec
KI = 5.0
Timestep clearly has effect on system stability.
Increasing T decreases stability of system.

## Slide 18: Effects of Saturation
Like in continuous-time systems, control saturation typically slows down system response
Consider PI control of same system:
X(z)
Y(z)

## Slide 19: Effects of Saturation
Using KP = 1.5, KI = 1, T = 0.5 sec:
Without Saturation
With Control Saturation
Saturation limit

## Slide 20: Effects of Saturation
Using KP = 1.5, KI = 1, T = 0.5 sec:
Without Saturation
With Control Saturation

## Slide 21: Digital Controllers: Compensators
PID controllers only allow you to place closed-loop poles in specific area
Digital compensators allow you to place pole(s) in specific desired locations
X(z)
Y(z)
Digital Compensator
Plant with ZOH input

## Slide 22: Digital Controllers: Compensators
Compensators allow you to shape frequency response of system
Lead Compensators
Lag Compensators
Used for improving stability margins
Increases system bandwidth – system responds faster
May increase sensitivity to noise though
Reduces system gain at higher frequencies without reducing it at lower frequencies
Slows down system response, but less susceptibility to noise

## Slide 23: Digital Controllers: Compensators
Compensators allow you to shape frequency response of system
Lead-Lag Compensators
,
Formed by cascading lead and lag compensators together in series
Low-frequency gain can be increased (leads to reduction of steady-state error) while also allowing increases in system bandwidth and stability margins
PID controller is actually special case of phase lead-lag compensator.

## Slide 24: Example: Digital Compensators
Let’s look at a Mechatronic system which can be controlled through lead-lag compensation
Euler’s Rotational Dynamics Equation:
J = inertia of head assembly
C = viscous damping coeff. of bearings
K = return spring constant
Ki = motor torque constant
𝜃 = angular position of read head
i = input current
Transfer function from i(s) to 𝜃(s)

## Slide 25: Example: Digital Compensators
Let’s look at a Mechatronic system which can be controlled through lead-lag compensation
J = 0.01 kg-m2
C = 0.004 N-m/(rad/s)
K = 10 N-m/rad
Ki = 0.05 N-m/mA
Open-Loop Transfer Function
Y(s)
R(s)
Digital Compensator
Zero Order Hold
Plant

## Slide 26: Example: Digital Compensators
Let compute the PTF for this system with T = 0.005 sec
Y(s)
U(s)
G(z)
Partial fractions expansion, etc…

## Slide 27: Example: Digital Compensators
Computing difference equations:

## Slide 28: Example: Digital Compensators
Simulating this system:
r = 1 ;
T = 0.005 ;
alpha = -0.85 ; %-.85
beta = 0 ; %0
b = -1.973 ;
c = 0.998 ;
A = 6.233e-05 ;
B = 6.229e-05 ;
t(1) = 0;
t(2) = T ;
y(1) = 0 ;
e(1) = r-y ;
u(1) = e(1) ;
y(2) = -b*y(1) + A*u(1) ;
e(2) = r-y(2) ;
u(2) = alpha*e(1) + e(2) -beta*u(1) ;
tf = 0.12;
i=3 ;
while(t(end)<tf);
% Calculate state dynamics
y(i) = -b*y(i-1) - c*y(i-2) + A*u(i-1) + B*u(i-2) ;
% Compute error
e(i) = r-y(i)*4.07e3 ;
% Compute control
u(i) = alpha*e(i-1) + e(i) -beta*u(i-1) ;
t(i) = t(i-1)+T ;
i = i + 1;
end

## Slide 29: Example: Digital Compensators
Let’s apply a step input to the open loop system and examine response
Y(z)
U(z)
Response is highly oscillatory
Indicates the system is very underdamped
Need to design compensator that adds more damping

## Slide 30: Example: Digital Compensators
To understand this, examine the poles of the open loop PTF
Roots of denom. polynomial
Real
Imag.
Open loop pole locations
Open loop system is very close to marginal stability boundary (occurs at

## Slide 31: Example: Digital Compensators
Closing the loop:
Y(s)
R(s)
𝛼 = -0.85
𝛽 = 0
KF = 4.07103
GD(z)
G(z)
Closed Loop PTF:
Characteristic Equation:
Roots of Characteristic Eq.
Poles shifted farther from unit circle!

## Slide 32: Example: Digital Compensators
Closed loop step response
Read Head Response
Motor Current Required
Settling time ~60 ms. Slow for this application but much better than open-loop response.

## Slide 33: Example: Digital Compensators
Suppose we want to reduce settling time still more. This will allow us to read from disk faster.
How should we set our gains: 𝛼, 𝛽, and KF?
One way is to examine the closed loop poles for a wide range of gains
  Select gains that move poles closest to origin
Form of characteristic equations for closed loop PTF:
b = -1.973
c = 0.998
A = 6.23310-5
B = 6.22910-5
Select a loop gain KF
Create array of different candidate 𝛼’s and 𝛽’s
Solve for roots of above equation, pick root with highest magnitude. This is “best” gains for this KF
Repeat for various KF values until desired performance achieved

## Slide 34: Example: Digital Compensators
Loop gain KF = 4070
𝛼 = -0.85
𝛽 = 0
Optimal Gains:
This is a plot of max
max= 0.63

## Slide 35: Example: Digital Compensators
Loop gain KF = 9000
𝛼 = -0.75
𝛽 = 0.3
Optimal Gains:
Significant reduction in settling time (~30%).
max= 0.51

## Slide 36: Example: Digital Compensators
Loop gain KF = 20000
𝛼 = -0.65
𝛽 = 0.8
Optimal Gains:
Further reduction in settling time (total of ~40%). Now have large overshoot though.
max= 0.38

## Slide 37: Digital Control: Conclusions
The field of digital control allows us to explicitly model and analyze the effects of implementing controllers with digital devices
Basic trends that emerge:
  Sampling time has a big effect on 1) stability, and 2) performance
Design of digital control systems involves tradeoffs!
Sampling Rate
Gain Selection
Saturation Limits